## Slide 1
Developing
for the
Commodore 64

## Slide 2
Outline
About Me
Why Program for the C64
About the C64
Getting Started
Examples
Next Steps
Q&A

## Slide 3
About Me (Michael Battaglia)
First started programming on the TI-99 in the mid 80s.
  BASIC
Moved over to the C64 from the late 80s to early 90s.
  BASIC V2
Then onto Windows 3.1 / DOS 6.22 from the mid 90s.
  QBASIC, VB6, C++
Onto Windows 95/98 in the late 90s.
  VB6
Onto Windows 2000/XP/VISTA/7 in the 2000s.
  VB6, C++, Java, C# (Windows CE), PalmOS (AppForge)
Onto Windows 8/10 from the 2010s through today.
  VB6, C#, ASP .NET, Android/iOS (Cordova), X86, 6502

## Slide 4
Why Program for the C64
8-bit computing never really went away.
  Emulators for 8-bit computers and consoles.
  NES Classic, C64 Mini/Maxi
C64 is the highest-selling single computer of all time.
  Between 12-17 million units sold.
Many new games and demos are still being created to this very day!

## Slide 5
Planet X2

## Slide 6
Super Mario Bros 64

## Slide 7
Fix-it Felix Jr

## Slide 8
About the C64
Released by Commodore in 1982.
6510 CPU – 8 bit at ~1 MHz with 64 KB of RAM (20 KB ROM).
  Registers: A, X & Y, P, PC, SP.
VIC-II – 16 colors, 8 hardware sprites, used mapped memory.
  40 columns x 25 rows (character mode)
  320x200 pixels (HiRes mode)
  Multicolor modes available but reduced the number of columns.
SID – 3 voices, ADSR envelope
  Arguably the best sound chip from this area of computing.

## Slide 9
Breadbox (1982)
64C (1986)

## Slide 10
About the C64
By default, the C64 reserved 26 KB of RAM
  BASIC, KERNAL, ZP, STACK, I/O, Characters
  Leaves 38 KB of RAM for the programmer
  You can switch out the BASIC and KERNAL to get an additional 16 KB of RAM.

## Slide 12
Getting Started
VICE https://vice-emu.sourceforge.io/
CBM prg Studio https://www.ajordison.co.uk/
6502 Assembly ML
Optional – Actual C64 with SD2IEC

## Slide 13
Getting Started
Why Assembly language?
  Pros:
        Very fast
        Highest level of control
  Cons:
        Harder to read and write
        Portability issues

## Slide 14
Getting Started
255 = Decimal
%11111111 = Binary
$FF = Hexadecimal
Base & Power | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
Decimal Value | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Example | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Number schemes:
  Decimal (0-9)
  Binary (0-1)
  Hexadecimal (0-F)
8 bit (Byte) – 0 to 255

## Slide 15
Getting Started
16 bit (Word) – 0 to 65535
4 bit (Nibble) – Representing Hex ($FA)
16 bit, 2 byte number (Word) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
High Byte (MSB) |  |  |  |  |  |  |  | Low Byte (LSB) |  |  |  |  |  |  | 
215 | 214 | 213 | 212 | 211 | 210 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
8 bit, 2 nibble number (Byte) |  |  |  |  |  |  | 
High Nibble |  |  |  | Low Nibble |  |  | 
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20

## Slide 16
Getting Started
Instructions – 56 opcodes
  lda – Loads value into the Accumulator
  sta – Stores value from the Accumulator
lda #2 ; decimal 2 (value) -> A sta $0400 ; A -> 400 hex (address)
lda $0400 ; 400 hex (address) -> A
sta $0401 ; A -> 401 hex (address)

## Slide 17
Getting Started
Addressing
  Zero Page – First 255 bytes of RAM
lda #2 ; immediate (2 cycles) lda $02 ; zero page (3 cycles)
lda $2000 ; absolute (4 cycles)

## Slide 18
Getting Started
Indexing
myList byte $4F, $5A, $B2, $CE, $30, $25, $F9, $1D
ldx #2
lda myList,x ; 3rd item in list -> A (4 cycles*)
lda #<myList ; LSB
sta $FD
lda #>myList ; MSB
sta $FE
ldy #06
lda ($FD),y ; 7th item in list -> A (5 cycles*)

## Slide 19
Getting Started
ldx #<$0401 stx $FD ldx #>$0401 stx $FE
Memory Address | Byte Value
$fd | $01
$fe | $04
Adding Word to Memory

## Slide 20
Getting Started
@label
sta $1000,y
ldx #<$0401 stx @label+1 ldx #>$0401 stx @label+2
OpCode | LSB | MSB
$99 | $00 | $10
$99 | $01 | $10
$99 | $01 | $04
Self-modifying Code

## Slide 21
Getting Started
Flow Control
  jmp – Jumps to an absolute memory address.
  jsr/rts – Jumps to a subroutine and returns.
  Branches – Jumps to a memory address based on the values in the P register (example: beq)
Negative Flag | Overflow Flag | (Unused) | Break Command | Decimal Mode | Interrupt Disable | Zero Flag | Carry Flag

## Slide 22
Examples
CBM prg Studio / Debugging
Indirect indexing vs. Self-modifying code
Writing string to the screen
Subroutines
Printing multiple strings

## Slide 23
Next Steps
Input from Keyboard / Joysticks
Sprites / Custom Character Maps
Interrupts
Sound Effects / Music
Loading / Saving

## Slide 24
Q & A
Commodore 64 Programming Reference Guide
Retro Game Dev https://www.retrogamedev.com/
C64 Memory Map http://sta.c64.org/cbm64mem.html
Codebase 64 https://codebase64.org/
Lemon64 Forums https://lemon64.com/forum
Michael Battaglia (aka VBGuyNY) https://battaglia.ddns.net/